## Slide 1: Delivering iOS 7
How Apple’s software updates impacted network demands.
Jeff Farese & Mike Lang

## Slide 2: What is the iOS 7 update?
Apple iOS is the operating system that runs on all iPhones, iPads, iPods
IOS 7 is the current major version of iOS and was released to public on September 18, 2013 at 1 PM EDT
Devices received OTA (over-the-air) update from the Internet or from a new version of iTunes, 11.1
The average size of this update was approximately 750MB

## Slide 3: Why was the iOS 7 upgrade a big deal?
The iOS 7 update created an unprecedented demand on networks – a first for a software update on the Internet
Released simultaneously to all devices
130 million of 415 million eligible devices upgraded in the first 10 hours1
Adoption rate of 50% within 48 hours2
There are ~22,000 Apple mobile devices at UCONN, ~18,000 connected on 9/18

## Slide 4: What are UCONN’s average network conditions?
Baseline by using previous day, Tuesday - 9/17.
Internet Traffic Total: 24.6 TiB (~24,600 GB)
Apple Software Update (iOS & iTunes) Traffic: 0.5 TiB – 11th in Top Application Traffic, 1.9% total traffic.
Peak (2 Hour Average) Throughput: 3.75 Gbps Inbound / 0.75 Gbps Outbound

## Slide 5: What change in demand did the iOS 7 release create?
Internet Traffic Total: 30.3 TiB (5.7 TiB increase, 23%)
Apple Software Update Traffic: 7.2 TiB (6.7 TiB increase, 14x) – 1st in Top Application Traffic, 23.8% total traffic.
Peak (2 Hour Average) Throughput: 5.0 Gbps Inbound / 0.75 Gbps Outbound (Bottlenecked at 5 Gbps sharply at 1 PM for 3 hours – we’ll get to why later…)

## Slide 6: Apple Software Update 9/18

## Slide 7: UCONN Internet Utilization 9/17 – 9/20

## Slide 8: Connecticut Education Network (CEN)

## Slide 9: Akamai(Content Distribution)

## Slide 10: How did others do?
  "In the five plus years I have been at Blue Coat, I've never seen a file update shake up the Internet like the iOS 7 update,“ Blue Coat's Jeff Brainard
  Ohio State University, Michigan University, New York University, Western Connecticut State University, University of Cincinnati all had reported network issues3,4

## Slide 11: How did this event impact UCONN?
Overall the increased demand had little impact on network service
Noticeable but minor latency increase for Internet traffic
Internet throughput was bottlenecked at 5 Gbps for a short period of time (causing minor latency, no drops)
No customer complaints or Service Center calls!

## Slide 12: Lessons Learned/Improvements
Observed unexpected 5 Gbps bottleneck on 10 Gbps design of network core – resolved 11/12/13.
Abnormal latency was quickly identified by network monitoring, allowed bottleneck to be addressed before user complaints or packet drops.
Bandwidth doubling every 24 months…

## Slide 13: Sources
http://www.electronista.com/articles/13/09/20/upgrading.spike.doubled.some.isp.traffic.12.percent.worldwide.internet.usage.jump/
http://routingfreak.wordpress.com/2013/09/23/ios7s-impact-on-networks-worldwide/
http://www.usatoday.com/story/tech/personal/2013/09/19/wireless-networks-college-ios-strain/2837341/
http://9to5mac.com/2013/09/18/ios-7-downloads-causing-network-outages-at-several-school-campuses-activation-server-failures/

## Slide 14: Thank You
Q & A